## Slide 1: Predictive Sensory Modeling: Use of Design of Experiments (DOE) and R to Optimize Dry Hop Mixtures for Aroma and Flavor Trent Leslie, Becca Ransohoff, Douglas Scott, Chandler Cottrell MadTree Brewing Cincinnati, OH

## Slide 2: Agenda
Introduction to Design of Experiments (DOE, DOX)
Mixture Experiments
The Experiment
  Experimental Design, Hardware, Data Collection
Data Format
Script Overview & Output
Putting It All Together
Q&A

## Slide 3: Design of experiments
Understanding complex systems (such as beer) by intentionally designing and executing experiments that help us investigate how variables in a system interact
Design experiments with terms that help you develop mathematical models to better understand relationships between variables

## Slide 4: Comparison of approaches
One-Variable-at-a-Time Approach
Only look at a slice of an area of flavor space
Can’t see interaction effects
Minimum of two weeks in between tasting any test batches
Can’t compare changes in recipe or process between finished products
Inefficient – Can’t necessarily attribute changes in response to specific process or variable changes
DOE Approach
Learn about a selected “region” of the flavor space
See how all factors interact at once in the same base beer
Help minimize effects from natural variation in fermentation
Efficient – model all interactions at once, confirmation of model predicted optimum can be used for additional testing

## Slide 5: Types of experiments
What type to use depends on the type of data you are collecting and the questions you are asking
  Simple comparison, factorial design, mixture experiment, response surface

## Slide 6: Mixture experiments
2-dimensional slice of a 3-dimensional factorial space
Factors are interdependent – the sum of all factors = 1

## Slide 7: Mixture experiments – ternary plot

## Slide 8: 18 runs – full model
Run | A:Hop A | B:Hop B | C:Hop C | D:Hop Load
1 | 0.5 | 0 | 0.5 | -1
2 | 0.5 | 0.5 | 0 | 1
3 | 0 | 1 | 0 | -1
4 | 0 | 0 | 1 | 0
5 | 0.5 | 0.5 | 0 | -1
6 | 0 | 1 | 0 | 1
7 | 0.5 | 0 | 0.5 | 0
8 | 0.5 | 0 | 0.5 | 1
9 | 0 | 0 | 1 | 1
10 | 0 | 0 | 1 | -1
11 | 1 | 0 | 0 | 1
12 | 0 | 0.5 | 0.5 | 1
13 | 0 | 0.5 | 0.5 | -1
14 | 1 | 0 | 0 | 0
15 | 0.5 | 0.5 | 0 | 0
16 | 0 | 0.5 | 0.5 | 0
17 | 1 | 0 | 0 | -1
18 | 0 | 1 | 0 | 0
Model Terms: A, B, C, AB, AC, AD, BC, BD, CD, ABD, ACD, BCD, AD^2, BD^2, CD^2, ABD^2, ACD^2, BCD^2

## Slide 9: 12 runs
Run | A:Hop A | B:Hop B | C:Hop C | D:Hop Load
1 | 0.5 | 0.5 | 0 | 1
2 | 1 | 0 | 0 | 0
3 | 0 | 0.5 | 0.5 | -1
4 | 0.5 | 0 | 0.5 | -1
5 | 0.5 | 0.5 | 0 | -1
6 | 0 | 0 | 1 | 0
7 | 0.5 | 0 | 0.5 | 0
8 | 0 | 0.5 | 0.5 | 1
9 | 0 | 0.5 | 0.5 | 0
10 | 0.5 | 0.5 | 0 | 0
11 | 0.5 | 0 | 0.5 | 1
12 | 0 | 1 | 0 | 0
Model Terms: A, B, C, AB, AC, AD, BC, BD, CD

## Slide 10: 9 runs
Run | A:Hop A | B:Hop B | C:Hop C | D:Hop Load
1 | 1 | 0 | 0 | 0
2 | 0 | 1 | 0 | 0
3 | 0.5 | 0.5 | 0 | -1
4 | 0.5 | 0 | 0.5 | 1
5 | 0.5 | 0.5 | 0 | 1
6 | 0 | 0.5 | 0.5 | 1
7 | 0.5 | 0 | 0.5 | -1
8 | 0 | 0.5 | 0.5 | -1
9 | 0 | 0 | 1 | 0
Model Terms: A, B, C, AB, AC, AD, BC, BD, CD

## Slide 11: Our experiment
Goal – Finalize a dry-hop recipe for a new Double IPA recipe
Mixture experiment
  Experimental Variables – 3 different hops
    Hop A – 0-100%
    Hop B and C – 0-50%
  Experimental Ranges – Range of 0-1.5x dry hop rate (1.9 lbs/bbl)
  Things we did not study – any hot side changes, limited to 3 hops, yeast strains

## Slide 12: The Hardware
The following costs are associated with a 10-vessel collection system
  Rack with Casters – $200
  Stainless 1.5-gallon Kegs – $80 x 10 - $800
  CO2 Manifold and Tubing – $200
  Various fittings – $400
  CO2 Tank – $50
  Temperature Controlled Storage (chest freezer) - $800
  Scale – $500
  Total ~$3,000

## Slide 13: Sensory data collection
  15 panelists – from trained research panel
    Incomplete block – 2 groups each receiving 10 samples in one sitting
  Scaling 7 aroma attributes, 8 taste attributes and overall preference
  Collected over a one-week span

## Slide 14: Analysis in R
Full analysis in R – a free and open source statistical programming language
  Blocking of panelists
  Development of contour plots
  Optimization
In depth into the development of the script and its application can be seen in But Sometimes You Get What You Need: Using R to Optimize Dry Hop Mixtures for Aroma and Flavor

## Slide 15: Background & Resources
  2016 WBC Talk: Improving Brewhouse Efficiency by Adjusting Mash Thickness and Lauter and Sparge Volumes (Eddie Gutierrez and Drew Russey)
  2017 ASBC Talk: Simplify QAQC Analyses and Decision Making with Open Source Software (Drew Russey)
  2017 MBAA TQ: Improving Brewhouse Efficiency by Adjusting Mash Thickness and Lauter and Sparge Volumes (Eddie Gutierrez and Drew Russey)
  2019 ASBC Workshop: From Bytes to BeeR: Leveraging the Statistical Programming Language R in Brewing Data Science (Drew Russey, Lucas Chadwick, Trent Leslie)
    http://bit.ly/ASBCCodingWorkshop2019 (Video tutorials!)
  2021 ASBC Talk: You Can’t Always Get What You Want - Use of Design of Experiments (DOE) to Optimize Dry Hop Mixtures for Aroma and Flavor (Becca Ransohoff, Chandler Cottrell, Trent Leslie, Doug Scott)

## Slide 16: Input Data Format
  Excel Spreadsheet (but that can be changed in the script)
  First seven columns need to be there
    However, the hop name columns can be changed to reflect whatever the experiment entails, but the script will need to be updated for that as well
  Columns eight and on can be as many or as few as you want and can be anything

## Slide 17: The script
  Script and Powerpoint files are available on GitHub
    https://github.com/trentleslie/ASBC_2021

## Slide 18: The output

## Slide 19: Putting it all together
This brings us to the hard part: using your own judgement and conversations to determine what’s important and what’s most likely to lead to the best possible product.
Sensory is often messy, but design of experiments and this script may help provide guidance.

## Slide 20: acknowledgements
Flavor Space Force Research Group
Becca Ransohoff
Doug Scott
Chandler Cottrell
Ryan Blevins
Garrett Schnieber

## Slide 21: Questions?